## Slide 1: Help
Stefanie Becker
Senior Safety Officer of Wicked Wings
Secretary of Wicked Wings
President of Queensland Sports Aviators
with Airspaces (and VHF calls)

## Slide 2: Official airspace resource: VNC (visual navigation charts)
VNC available under Wicked Wings site info: https://www.wickedwings.com.au/about
Pro:
Accurate and up to date
Cons:
Hard to see anything
Can take a long time to upload with good resolution

## Slide 3: Better resource (for Australia):
Interactive online map: https://xcaustralia.org/aircheck/aircheck.php
Will use this almost exclusively for this presentation.
Also allows checking if you violated airspace during your flight

## Slide 4: Where can I / can’t I fly?
On this map -- https://xcaustralia.org/aircheck/aircheck.php – go to Airspace Layers
Set slider to a realistic height for the day, to limit view to relevant airspaces
Thermal forecast:
Ausrasp
A / C / D: controlled airspace. We only have Class C
(marked yellow).
Do not fly there
BUT: OK to fly in class E (marked green): monitor VHF on area freq
CTR: Control zone for airports and military (red)
Do not fly there!

## Slide 5: Where can I / can’t I fly?
On this map -- https://xcaustralia.org/aircheck/aircheck.php – go to Airspace Layers
CTAF compulsory VHF:
10 nm around smaller airports (e.g., Toowoomba, Warwick). Marked turquoise.
Ok to fly there with a VHF; do not interfere with starts or landings (= do not fly low over airstrip).
Some VHF rules.
Danger: Starts with D… (e.g., D654 Amberley), military training / low flying. Marked pink.
OK to fly there!
Restricted: Starts with R… (e.g., R639 Amberley, marked violet). Mostly military; usually active on weekdays, inactive on weekends. Check ATIS or NOTAMs.
Do not fly when active. OK to fly when inactive.
Notes: CTAF: Common Traffic Advisory Frequency. Airfields where pilots themselves coordinate taxiing, starting and landing.

## Slide 6: Airspace Boundaries
https://xcaustralia.org/aircheck/aircheck.php – If you hover the mouse over an airspace, you will see the airspace boundaries (upper / lower)
SFC: Surface / Ground
Airspace goes from ground to 6,500ft
To stay out, we need to fly above 6,500ft
FL125 = 12,500 ft (always FL+00 = feet)
Airspace goes from 8,500ft to 12,500ft
To stay out, we need to fly below 8,500ft
UNL = unlimited (in practice: FL175 or 245)*
Airspace goes from ground to 17,500ft
To stay out, we need to fly around this airspace
Notes: There is always controlled airspace class A above all other airspaces. Inside radar controlled areas, it starts at 17,500ft (FL175), outside it starts at 245,000ft (FL245). As our maximum height is usually 10,000 – 12,500ft (depending on whether we have an oxygen endorsement), this means we have to fly around airspaces if their upper boundaries are >12,500ft (see slide 20 for max heights).
As we cannot maintain height, it is not always advisable to try to fly above an airspace (unless we are sure we can remain clear of the boundaries).

## Slide 7: Rules CTRs: Don’t fly there!
https://xcaustralia.org/aircheck/aircheck.php
Only CTRs displayed: There are other controlled airspaces around the CTRs!
You see:
CTRs: Control zone for airports and military (red)
Never fly there!
Even for military, airspace when all restricted zones are de-activated: Do not fly into CTR Amberley or CTR Oakey (top left)
CTR Oakey
SFC: from ground
CTR Brisbane
CTR Archerfield
CTR Gold Coast
CTR Amberley

## Slide 8: Rules class A, B, C, D: Don’t fly
https://xcaustralia.org/aircheck/aircheck.php
Visible only CTRs and controlled airspaces A, B, C, D (class C, in this case)
You see:
Yellow Brisbane/Gold Coast Airspace (class C, various heights)
Never fly into these airspaces. They are always active or: You can assume this airspace is active.

## Slide 9: Rules Class E: Fly with VHF
https://xcaustralia.org/aircheck/aircheck.php
Visible: CTRs (red), Airspace class C (yellow) and Class E (green)  need to move slider up to 8,500ft to see Class E Airspace
Overlaid:
Green Airspace Class E, here: from 8,500ft
We are allowed to fly in class E airspace
Only required to monitor VHF on area frequency
(here: 121.2).

## Slide 10: Rules Restricted Areas (R): Don’t fly when they are active
https://xcaustralia.org/aircheck/aircheck.php
These are mostly military airspaces (Amberley and Oakey), usually only active during the week (not on weekends or public holidays).
Marked violet, various heights.
We’re not allowed to fly in there when it’s active.
This airspace (R625C) is over Ma Ma Creek, Stringybark and Tenthill sites.
Wilson’s is in R625D, height from 8,500ft.

## Slide 11: How do I know if R… is active?
Know the pattern:
Amberley is active every weekday 9am to 5pm. Oakey is active every weekday 9am to 5pm, except Friday (de-activate at 12pm).
Call ATIS (Automatic Terminal Information Services): Recording
ATIS Amberley: (07) 5361 3581 (VHF: 123.3)
ATIS Oakey: (07) 4577 7235 (VHF: 123.4)
Active: Status A (Alpha), B (Bravo), C (Charly), etc..
De-activated: Z (Zulu)
Notes: https://www.airservicesaustralia.com/naips/Fua
Check this link to learn more about the operations in the restricted military areas: https://www.casa.gov.au/search-centre/stay-ontrack-flying-brisbane-region/general-military-information?fbclid=IwAR0v5_qMeuBrtv5g_eq0Lo8Mo72Eve3_dkh4E07s5yUcyVEm1u-bUgwgK1o#Militaryairspace

## Slide 12: How do I know if R… is active?
Do Restricted Area Briefing with Airservices
Register with Airservices here, using your SAFA number (pilot license): https://www.airservicesaustralia.com/naips/
In NAIPS, go to Restricted Area Briefing and look up codes for restricted areas and enter the ones of interest into Restricted Area
Amberley: R625A, R625B, R625C, R625D, R639A–D start at 10,000ft
Oakey: R654A, R654B, R654C, R654D
Not that easy to interpret, but nowadays, AI can help!
Notes: https://www.airservicesaustralia.com/naips/Fua
Check this link to learn more about the operations in the restricted military areas: https://www.casa.gov.au/search-centre/stay-ontrack-flying-brisbane-region/general-military-information?fbclid=IwAR0v5_qMeuBrtv5g_eq0Lo8Mo72Eve3_dkh4E07s5yUcyVEm1u-bUgwgK1o#Militaryairspace

## Slide 13: Restricted Area Briefing
On the website: Select Restricted Area briefing and input areas
Notes: https://www.airservicesaustralia.com/naips/Fua

## Slide 14: How do I read the briefing?
Let’s enter R625C for Amberley and R654C for Oakey, to find out if they are activated. I asked for the briefing on 19/12/23 at 6.45am.
R654C is deactivated at this time: we would be good to fly in there
Red/green: R625C is de-activated at this time but scheduled to be active on 18/12/23 at 23:30+10 to 19/12/23, 13:00+10
This means: Active on the 19/12/23 from 9.30am to 11pm. Outside these times, we would be good to fly in there, but once those times roll around, we need to stay out.
Date
Date
Time
Time
Dates are backwards: Year / Month / Day
Time in UTC: Brisbane – 10 hours
(I asked for 24 hr briefing)
Notes: We can also ask for clearance through airspace when it is active. I would not recommend trying this as the tower may ask you for things we don’t have, like SSR codes / transponder codes when you request clearance. Anyhow: For airways clearance through restricted areas, contact Oakey Delivery on VHF 133.35. Request clearance through Amberley by contacting Amberley Delivery on VHF 134.6.

## Slide 15: How do I check NOTAMs?
Register with Airservices (NAIPS), log in and select “Location Briefing” OR:
  Use this link: https://www.airservices.gov.au/naips/Briefing/Location
Select relevant location and click “NOTAM”
NOTAMs
You can use any AI or Google to find this!

## Slide 16: How do I check NOTAMs?
Example Result:
Danger area
(ignore)
Restricted area
(can’t fly)
Timestamps translate to:
8:00 am – 11:00 pm
Friday, 16 October 2026
Once you are on this page, you can feed this information into any AI / Google to extract the activation times.

## Slide 17: Area Briefing
You can also use the area briefing from Airservices to learn whether Oakey/Amberley CTR will be active on certain days, and to get more info about weather, planned flight operations, etc.
Go to Airservices  NAIPS  Area Briefing
        Look up the codes for the area you’re interested in (41)
Enter these codes (9410 etc.) into the area briefing

## Slide 18: Area Briefing Results:
You will get results for (among other things):
Amberley, Oakey, Brisbane, Archerfield, Gold Coast and Sunny Coast
Weather info
Activation Status
BUT only of CTR.
Restricted Airspaces must still be checked!

## Slide 19: Airspace: CTAF (optional or mandatory VHF)
https://xcaustralia.org/aircheck/aircheck.php
Mandatory: RMZ. Optional: G (e.g., Dalby)
Marked turquoise:
We are allowed to fly into both CTAFs.
In RMZ, aircraft should officially make a VHF call when inside 10nm and under 5,000ft. But: This is a rule for planes to coordinate starts and landings (~200kt).
Paragliders: Monitor CTAF frequency, and do not fly low near the airstrip. Make a VHF call if necessary to avoid collisions.
UNL: Unlimited
(but: misleading)
Better: Upper 5,000ft

## Slide 20: VHF frequencies
In Airspace E (often above 5,000ft; definitely above 8,500ft at our sites):
No need to make VHF calls or get permission, but:
Monitor VHF area frequency (above 8,500ft in our area: Brisbane 121.2).
Sailplanes have permission to use different frequencies and use those.
In CTAF: Use frequencies posted on the internet and the airspace map
Good for us:
Same frequency for Oakey, Toowoomba airspace (127.65).
Warwick: 127.85
Stanthorpe: 126.7
When flying Killarney and paragliders are venturing west towards Warwick, I would recommend making a VHF call to Warwick.

## Slide 21: VHF calls
Officially, when asking for clearance (= permission to enter controlled airspace), we would use callsign “Paraglider” + last 4 digits of SAFA number, give our position (including altitude) and ask for permission to enter controlled airspace (A, B, C, D) or restricted areas (R…) at military aerodrome.
However, the normal strategy is to try to keep out of restricted and controlled airspace. We just don’t go there.(!)
So how do we use VHF?
When operating a launch close to or within a CTAF or controlled airspace, we make periodic calls.
Example: “Warwick Traffic, Paraglider Control (callsign; NOT giving position), there are paragliding operations 10 miles east and north of Warwick, with paragliders at various altitudes (can give a range, e.g., 1,000ft to 6,000ft), Warwick (Traffic).”
 same for area frequency calls, just use “All Traffic”.
Makes most sense when there is a lot of traffic around

## Slide 22: VHF calls
So how do we use VHF?
When you see another aircraft nearby and want to alert them to your presence:
Example when you are close to an aerodrome (Warwick):
“Warwick Traffic, Paraglider [last four digits of your SAFA number] 9 miles south of Warwick at 8,500 ft, tracking north, Warwick (Traffic).”
Example when you are NOT close to an aerodrome (on area frequency):
“All Traffic, Paraglider [last four digits of your SAFA number] 15 miles east of Warwick at 8,500 ft, tracking north.”

## Slide 23: Normal flying in Airspace G
Airspace G is uncontrolled airspace  everything that is not marked in a map.
Is usually used for recreational flying, motorplanes, sailplanes, hang gliders, paragliders, etc.
Allowed to fly there when operating under visual flight rules (VFR):
VFR flight rules:
Below 3,000ft AMSL or 1,000ft AGL: Clear of cloud
Below 10,000ft (roughly 3,000m): 5km horizontal visibility, 1,500m distance from cloud horizontally, 1,000ft vertical (~300m)
At or above 10,000ft AMSL: 8km horizontal visibility, same distance from clouds
See part 91 CASR, General operating and flight rules

## Slide 24: Overview VFR flight rules
Notes: This is from CASR part 91. See also CASA https://www.casa.gov.au/sites/default/files/2022-02/visual-flight-rules-guide-interactive.pdf

## Slide 25: Maximum heights in Airspace G & E
SAFA: Without oxygen endorsement, we can only fly to max height 10,000ft (~3,000m). [SAFA operations manual, 4.1.9]
CASA (part 91 CASR): With oxygen endorsement we must use oxygen when flying above 12,500 feet (~3,800m) for longer than 30 minutes.
In a nutshell:
We can fly up to 12,500ft / ~3,800m without oxygen – but apparently we’d need the endorsement to fly above 10,000ft / 3,000m.
Notes: 4.1.9 >10,000 Feet Above Mean Sea Level
4.1.9.1 Hang Gliders, Paragliders, Powered Paragliders & Weightshift Microlights
No hang glider, paraglider, powered paraglider or weightshift microlight shall be flown at a height above 10,000 feet above mean sea level except where the pilot:
(a) Is not limited by controlled airspace; and
(b) has an Oxygen Endorsement; and
(c) is carrying and using an approved oxygen supply system, or
(d) is given written permission by CASA.

## Slide 26: Overview:
Which airspaces can I fly in?
Airspace | On xcaustralia.org | OK to fly?
CTR | Red circle | Never
Airspace class A, B, C, D around major airports. We only have E | Yellow regions | Never*
Restricted areas (R…). Military airspace like Oakey / Amberley | Violet regions | Not when active* (most weekdays)
Danger Areas | Pink regions | OK to fly
CTAF | Turquoise circles | OK to fly if you have VHF. Can make calls on CTAF freq; do not fly low over airstrip
Airspace Class E | Green regions | OK to fly: Monitor VHF area freq (121.2)
* Using VHF radio, it is possible to ask for permission to enter all these airspaces. However, this is not recommended, and forbidden in Manilla (to contact Tamworth).

## Slide 27: Thank you!!!
Questions, Suggestions, Comments?
Send me an email:
s.becker@psy.uq.edu.au
Or find me on:
WhatsApp
(0449 883870)
Facebook